Added-value MEYLE repair kits for time-effective cardan shaft repair yield cost savings of up to 70%

- Another full-service MEYLE cardan shaft centre bearing kit with a full set of components required for flex disc change

- Replacing the cardan shaft centre bearing without changing the cardan shaft? The latest "MEYLE Mechanics" video demonstrates how!

Hamburg, 23. September 2015. Replacing the centre shaft bearing without changing the entire cardan shaft assembly? That this is not a necessarily a contradiction in terms is demonstrated in the latest "MEYLE Mechanics" video now published on the company's "MEYLE TV" YouTube channel. In 2014, Wulf Gaertner Autoparts AG launched a full-service cardan shaft centre bearing kit for the Porsche Cayenne and VW Touareg cardan shaft repair, thus enabling workshops to repair a faulty centre bearing swiftly without having to replace the complete cardan shaft, as is required for the original design. Now, yet another full-service kit is making its market debut: Supplied with all parts required for the cardan shaft centre bearing repair the kit also includes all components for the flex disc change.

In the event of a cardan shaft centre bearing failure on a Porsche Cayenne or VW Touareg, there used to be only one remedy: Changing the complete cardan shaft assembly. In 2014, Hamburg manufacturer Wulf Gaertner Autoparts was one of the first aftermarket vendors to supply an alternative cost-efficient solution by offering cardan shaft centre bearing sets which can be replaced separately. With all the necessary components coming in a single set (including the bearing, clamp ring, rubber boot and grease) repair professionals no longer have to re-install used components such as the rubber boot. The recently launched value-added kit also includes the flex disc complete with all screws required for replacement. Dispensing with time-intensive cardan shaft assembly replacement, the new centre shaft bearing yields cost savings of up to 70 per cent.

To ensure smooth and professional installation the kit comes with step-by-step fitting instructions. In addition, the entire repair process is demonstrated in a new video of the "MEYLE Mechanics" on the "MEYLE TV" YouTube channel. This is the link to the video: https://youtu.be/urqi_wjSY4M.

The new cardan shaft centre bearing is now available under the MEYLE no. 100 152 2001.

About the Company

Wulf Gaertner Autoparts AG develops, produces and sells top-quality and quality-certified spare parts for cars, vans and trucks for the independent aftermarket under the brands of MEYLE and MEYLE-HD. The Hamburg manufacturer’s portfolio currently includes more than 18,500 articles, covering practically every requirement on the market. Engineers at the company also focus on products and services which can improve processes within the workshop. The MEYLE engineers have developed around 750 parts for thousands of different vehicle models and have technically optimised such parts compared to those made by the original equipment manufacturers. These MEYLE-HD products are extremely resilient and have a long service life. There is a four-year guarantee on the unique feature of technically improved MEYLE-HD parts.

Wulf Gaertner Autoparts AG was founded in 1958 and is headquartered in Hamburg, Germany. The company operates in 120 countries. In addition to its state-of-the-art logistics centre in Hamburg, the company also operates subsidiaries and production sites worldwide.